## Slide 1: Genomic DNA qPCR Preparation

## Slide 2
Primer pair 1
1:1
Validating primers– each color is a different primer pair
Primer pair 2
Primer pair 3
Primer pair 4
Primer pair 5
Primer pair 6
Primer pair 7
Primer pair 8
Primer pair 9
Primer pair 10
Primer pair 11
Primer pair 12
1:4
1:16
1:64
Add primer pair master mixes column by column
Add gDNA dilution series concentrations row by row
Seal with lid, spin, bring to qPCR machine
gDNA
dil
Each plate should have the normalizer site as well to look at relative efficiency.

## Slide 3
Test Sample
Test Sample
Test Sample
Test Sample
Calibrator
Calibrator
Calibrator
Calibrator
Test run – each color is a different primer pair
Each plate should have >= 1 normalizer site, the rest can be test sites.

## Slide 4
What is the haploid genome length?
Convert the haploid genome length (G) to picograms (pg) using the Dolzel conversion where 1 pg typically contains 978 Mb: G_pg = G/978e6 =
Write the number of genome copies expected in the following pg quantities:
Num copies in 4000 pg = 4000/G_pg =
Num copies in 2000 pg = 2000/G_pg =
Num copies in 1000 pg = 1000/G_pg =
Num copies in 500 pg = 500/G_pg =
Num copies in 250 pg = 250/G_pg =
Num copies in 100 pg = 100/G_pg =
Num copies in 50 pg = 50/G_pg =
Num copies in 25 pg = 25/G_pg =
Num copies in 10 pg = 10/G_pg =
Num copies in 5 pg = 5/G_pg =
Num copies in 1 pg = 1/G_pg =
Num copies in 0.5 pg = 0.5/G_pg =
Num copies in 1000 pg = 0.25/G_pg =
Num copies in 1000 pg = 0.1/G_pg =
Num copies in 1000 pg = 0.05/G_pg =
Notes: YEAST:
12157105
0.012430577709611451
4000 -> 321787
2000 -> 160894
1000 -> 80447
500 -> 40223
100 -> 8045
50 -> 4022
25 -> 2011
10 -> 804
5 -> 402
1 -> 80
0.5 -> 40
Hap_G = 12.2e6
G_pg = 12.2e6/978e6 = 0.01247 pg per hap genome
80,000 copies = 80e3*0.01247 = 997.6 pg ~= 1000 pg
80 copies = 80*0.01247 ~= 1 pg
DF = 10
1:1 = 500 pg/ul x 2 = 1000 pg
1:10 = 50 pg/ul x 2 = 100 pg
1:100 = 5 pg/ul x 2 = 10 pg
1:1000 = 0.5 pg/ul x 2 = 1 pg
HUMAN:
Hap_G = 3.2e9
G_pg = 3.2e9/978e6 = 3.27
30000 copies = 30e3*3.27 = 98100 pg = 98.1 ng
30 copies = 98.1 pg
Do 10-fold dilution series starting at 50 ng/ul when using 2 ul in each reaction.
1:1 = 50 ng/ul x 2 = 100,000 pg
1:10 = 5 ng/ul x 2 = 10,000 pg
1:100 = 0.5 ng ul = 500 pg/ul x 2 = 1000 pg
1:1000 = 0.05 = 50 pg/ul x 2 = 100 pg
Sciara
Hap_G = 292e6 for somatic haploid genome
G_pg = 292e6/978e6 = 0.2985685 pg per hap genome
I’ve been doing 4-fold dilutions starting at 1 ng/ul x 2 = 2 ng – and getting down to 15.625 pg/ul at the 1:64
Upper = 2 ng has 2000/0.2985685 = 6698.6 ~= 6700 copies
Lower = 15.625/0.2985685 = 52.33 copies
If I wanted to, I could possibly try
10 pg to 10,000 pg (10 ng) for 10-fold dilutions
1:1 = 5 ng/ul x 2 = 10 ng = 10,000 pg = 33493 copies
1:10 = 500 pg/ul x 2 = 1000 pg = 3350 copies
1:100 = 50 pg/ul x 2 = 100 pg = 335 copies
1:1000 = 5 pg/ul x 2 = 10 pg = 33.5 copies
Drosophila (dm6) = 143726002 bp = 143.73 Mb
Hap_G = 143.73e6
G_pg = 143.73e6/978e6 = 0.146963190184 pg per hap genome
6 ng has 6000/0.146963190184 = 40826.5 copies
1:1 = 3 ng/ul x 2 = 6 ng = 40826.5 copies
1:10 = 300 pg/ul x 2 = 600 pg = 4083 copies
1:100 = 30 pg/ul x 2 = 60 pg = 408.3 copies
1:1000 = 3 pg/ul x 2 = 6 pg = 40.83 copies

## Slide 5
Determine the dynamic range (copy number and corresponding pg quantity) that you want to validate primers over.
The dynamic range should cover the range expected in future tests after validation.
On the lower end, the number of genome copies should probably not go below 30 to keep random variation small relative to the mean and to avoid having 0 copies of your specific locus of interest present. Moreover, the target low end (copy number) Ct value is 30.
On the higher end for copy number, the target Ct value is around 20. There is a 210 = 1024-fold difference from a Ct of 20 to 30. This means that once you pick your low-end, if you plan to validate across the entire dynamic range, then high end can be found by multiply by 1024 – or vice versa if the upper end is selected first. If you plan to do 4-fold dilutions, then multiply or divide by 64.
If you need a larger dynamic range, a Ct range of 19-32 could be ok.
Next, take the high-end pg amount (H), divide it by 2 (H/2 = h), and make that (h) your starting concentration: h pg/ul.
h =
Determine dilution factor by:
DF = e^(log(H/L)/3) =
Notes: For yeast:
L= 1 pg -> 80 genomic copies
H = 1000pg -> 80447 genomic copies
h = 500
DF = e^(log(H/L)/3) = 9.999999999999996 = 10
===========
DF calcs:
L*X^4 = H
X^4 = H/L
4log(X) = log(H/L)
Log(X) = log(H/L)/4
e^log(X) = e^(log(H/L)/4)
X = e^(log(H/L)/4)
Note – previously I erroneously had DF= log(highEnd/lowEnd)/log(4) =
NOTE: actually starting equation should have exponent of 3 (not 4) since only dilute 3x for the 4 conditions:
L*X^3 = H
So final equation is:
X = e^(log(H/L)/3)

## Slide 6
Replace example values below with values for your experiments
Validation plates for yeast:
Using 2 ul for the ng and pg calculations:
Ratio ng/ul pg/ul ng pg #genomecopies(coverage)
1:1 = 0.5 ng/ul 500 pg/ul 1 ng 1000 pg 80447
1:10 = 0.05 ng/ul 50 pg/ul 0.1 ng 100 pg 8045
1:100 = 0.005 ng/ul 5 pg/ul 0.01 ng 10 pg 804
1:1000 = 0.0005 ng/ul 0.5 pg/ul 0.001 ng 1 pg 8
Test plates:
Next, you need to determine what is the most sensible pg amount to use in future tests after validation. The pg quantity needs to allow for enriched regions to reach copy numbers under the high end of the validated range, but it also needs to allow for depleted regions (e.g. control sites) to stay above the low end of the validated range.
For example, if you expect enrichments to reach 40-fold, then 1000/40 = 25 – meaning you may want to start with 25 pg per reaction. This will allow a 25-fold depleteion (25/1) for the 1-1000 pg range we are testing. If you want to allow for 25-fold enrichment and 40-fold depletion, start with 40 pg. I imagine you should use somewhere between 25-40 pg DNA per reaction.

## Slide 7
Primer design:
PCR product size 60–120, minimum primer size = 18, optimum primer size = 20–21, maximum primer size = 25, minimum Tm = 57, optimal Tm = 61–62, maximum Tm = 66, maximum Tm difference = 1-, maximum 3’ self complementarity = 2, maximum self complementarity = 8 (preference given to lower), maximum poly-X = 4. In cases where other primers needed to be tested, we increased the maximum primer size to 135, the primer size range to 16–26, the Tm range to 55–66, the maximum Tm difference to 2–3, and the maximum poly-X to 5. A minimum of twenty candidate primer pairs were returned and screened for specificity in the genome.
If NCBI has the genome make sure to test the primers for specificity in that genome.
Else use my analyzePrimerPairs.py script to analyze the specificity.
Ordering invitrogen primers is cheap and they work great. IDT is as good (some will say better), but much more expensive. I’ve seen no difference whatsoever between pimers ordered from the two companies.
25 nmole is plenty; desalted and dry is fine (default)
Name oligo: o-name-fwd-01, o-name-rev-01
(if need to try another pair, that is 02, etc)
When Primers arrive:
For each primer, label two tubes – 1 for 10 uM and 1 for 1 uM
Re-suspend in UPW to make 100 uM stock
Make 10 uM working stock by adding 20 ul 100 uM stock to 180ul UPW
1 uM primer solutions (for 15 ul reactions):
- 180 ul of UPW
- 20 ul of corresponding 10 uM primer to each
Notes: PCR product size 60–120, minimum primer size = 18, optimum primer size = 20–21, maximum primer size = 25, minimum Tm = 57, optimal Tm = 61–62, maximum Tm = 66, maximum Tm difference = 1-, maximum 3’ self complementarity = 2, maximum self complementarity = 8 (preference given to lower), maximum poly-X = 4. In cases where other primers needed to be tested, we increased the maximum primer size to 135, the primer size range to 16–26, the Tm range to 55–66, the maximum Tm difference to 2–3, and the maximum poly-X to 5. A minimum of twenty candidate primer pairs were returned and screened for specificity in the genome.

## Slide 8
  An analysis of the primers I used in the past that did well had these qualities as reported by NCBI primer blast:
  mean Tm = 60.8895 - 61.0595 [[57.5 - 65.5 ]]
  basically mean Tm = 61.
  mean len = 21.7 [[15 - 26 ]]
  most were 24
  mean GC = 52.17 [[43.48 - 68.75 ]]
  majority were 50%
  mean self comp = 4.85 [[2.00 - 8.00]]
  --> this does not seem to matter as much as 3'
  mean self-3'-comp = 1.45 [[0 - 6]] -- mostly 0-2
  Primers that did less well had these qualities as reported by NCBI primer blast:
  mean Tm = 58.3236 [[ 53.21 62.12 ]]
  Basically mean Tm = 58, range 53-62
  meanlen = 20.2143 [[17 24]]
  mean GC = 51.5014 [[40.00 66.67]]
  mean self comp = 4.1428 [[2.00 8.00]]
  mean 3' self comp = 1.14286 [[0.00 3.00]]
  Primers that did bad had these qualities as reported by NCBI primer blast:
  mean Tm = 56.3817
  53.21 60.08
  mean len = 19.6667
  15 24
  mean GC = 48.7358
  40.00 61.11
  mean self comp = 4.91667
  2.00 9.00
  mean 3p self comp = 1.08333
  0.00 4.00
Ultimate summary:
The lower the Tm, worse performance.
Lower primer len, worse performance.
Lower GC, worser performance.
Probably b/c of what the qPCR machine is automatically set to for cycling parameter – i.e. melt, anneal, extend temps default to Tm=61-ish.
Notes: Product size mean = 78, median 77, range = 62-116
Primer pairs hat passed tests previously:
PrimerName Primer-seq PrimerLen Tm GC% Self-comp Self-3'-comp
MSF-1 passed 4 tests
MSF-Locus1-Fwd TTGCCAATTGCCTCTGGTTGAGAC 24 63.86 50.00 6.00 1.00
MSF-Locus1-Rev GACTTTGCTGTTTGCTGTCAGGCT 24 64.29 50.00 5.00 3.00
JU-9-1 passed 4 tests
JU9-Fwd CCCTAAGTTCGCTGGCTTTTT 21 59.11 47.62 3.00 0.00
JU9-Rev CCTACTGAGTTGGTCCTCTAGTGAAA 26 61.48 46.15 7.00 2.00
JU-13-A passed 1 test
JU13-A-Fwd TCCTGGGAAATCAGCCTACAAG 22 59-59.76 50.00 4.00 1.00
JU13-A-Rev CCTGACGGTGTCTGATCACTTAGA 24 59-61.64 50.00 6.00 3.00
Ghosh-B -- passed ~2 tests, failed 1 test (but was candidate for conditional pass)
Ghosh-B-Fwd TGCCATTACCGGTTCTCCA 19 58.62 52.63 6.00 2.00
Ghosh-B-Rev TTCAACCGCATAAGAGATGGTG 22 58.73 45.45 3.00 0.00
JU-15-B passed 1 test
JU-15-BC conditionally passed 2 tests (only a slight problems with relEff in each)
JU-16-C conditionally passed 2 tests (had to remove the 1:1 data points in each test)
JU16-C-Fwd TCGGATTTGGAAGCTACTAT 20 53.54 40.00 4.00 2.00
JU16-C-Rev GGTTATTACCCGTTGAGTTT 20 53.21 40.00 6.00 0.00
JU-16-CD conditionally passed 2 tests (had to remove the 1:1 data points in each test)
Ghosh-D passed 1 test, conditionally passed 1 test (needed to remove a single outlier)
Ghosh-D-Fwd TTCACAAGGGTCTCTGCTGACTC 23 62.12 52.17 5.00 3.00
Ghosh-D-Rev GCGGGACCGGACTTCCTA 18 60.76 66.67 4.00 2.00
JU-17-D passed 1 test
Ghosh-E passed 2 tests
Ghosh-E-Fwd CGCGCCCATTAATACCCTT 19 57.98 52.63 6.00 0.00
Ghosh-E-Rev AGGGCCGCGCTTTGA 15 58.71 66.67 5.00 1.00
MSF-11 passed 1 test
MSF-Locus11-Fwd TACTCACAGGACAAGGATGCGGTT 24 63.89 50.00 2.00 0.00
MSF-Locus11-Rev TGAATTAACTACGCGCGCCTACCA 24 64.74 50.00 8.00 2.00
JU-20-F passed 1 test
JU20-F-Fwd CACTTTGCACTGGAACTTACAACAC 25 61.18 44.00 5.00 1.00
JU20-F-Rev GTCCCCAAATGGGCAGAATA 20 57.55 50.00 6.00 2.00
JU-22-1 passed 1 test, conditionally passed 1 test (needed to remove a single outlier)
JU22-1-Fwd AAGGGAGGCGAGGATGTGT 19 60.61 57.89 2.00 0.00
JU22-1-Rev GGCTGGGTGCGGAGATT 17 59.34 64.71 2.00 1.00
Ghosh-G passed 2 tests
Ghosh-G-Fwd TTGTGTGCCCCGCTCC 16 59.53 68.75 2.00 0.00
Ghosh-G-Rev TTCCTGTTGGTGAAGCTAACGTT 23 60.68 43.48 6.00 6.00
MSF-16 passed 2 tests
MSF-Locus16-Fwd TGAACCAGAGTTTCATCTGCGACC 24 63.12 50.00 5.00 0.00
MSF-Locus16-Rev AGAAGCCGCTCCACATACAGTCCT 24 65.54 54.17 5.00 2.00
Ghosh-H passed 2 tests
Ghosh-H-Fwd TGGTCTTCCCCTACCCTCTCA 21 61.42 57.14 3.00 1.00
Ghosh-H-Rev TGGAGTCTTGCGAGGCG 17 59.36 64.71 4.00 2.00
JU-28 passed 2 tests
JU-29-1 conditionally passed 1 test (needed to remove both 1:1, still did not pass relEff), failed 1 test
JU-30-1 conditionally passed 1 test, passed 1 test